## Slide 1: Design and Development of a RAM-based PUF
Zissis Tabouras (s284685)
Elena Roncolino (s304719)
Stefano Palmieri (s281677)

## Slide 2
What is a PUF?
2
Physical Unclonable Function
Extracts secrets from physical characteristics of a device
Useful to implement authentication mechanisms

## Slide 3
Why are PUFs important?
3
Reproducible
Unique
Unclonable
One-way
Unpredictable

## Slide 4
How does a PUF work?
4
Provide a challenge to the device
Device answers with the value matching that challenge

## Slide 5
SEcube™ and SRAM PUF
5
SEcube™: silicon embedding a processor, an FPGA and a smart card
SRAM in the SEcube™ used to extract PUFs

## Slide 6: Implementation

## Slide 7
Implementation
7
Two flows: 1. Host retrieves all the responses from the device 2. Challenge-response authentication mechanism between the host and the device
Notes: Store SRAM content into flash memory
Access flash memory to retreive PUFs
Store PUFs in DB

## Slide 8
Host
Requests list of PUFs
Receives PUF list
Stores the list in a DB
Device
Stores SRAM content in FLASH (startup)
Sends list of PUFs
First flow
Notes: PUF retrieval and DB initialization
Store SRAM content into flash memory
Access flash memory to retreive PUFs
Store PUFs in DB

## Slide 9
Host
Generates challenge
Sends challenge to board and DB
Compares responses (Hamming)
Device
Receives challenge
Sends response
Second Flow
Notes: Application of a challenge and verification of device authenticity
Apply challenge to DB and board
Retreive board response
Perform response matching

## Slide 10
Results
Thresholds:
  2 -> 79,00% of accurancy
  3 -> 90,10% of accurancy
  4 -> 93,67% of accurancy

## Slide 11: Example on the board

## Slide 12
Flow 1

## Slide 13
Flow 2